BAR2308TT
A SSI chip with all the functionality of all basic Logic gates
---- Designed by Amit Barman

---
This chip provide us all the functionality of all basic logic gates- OR, AND, NOT, NOR, NAND, XOR, XNOR and Half adder.
This project is open source at here

---
Icon of BAR2308TT

---
Layout of BAR2308TT

---
01
Use as OR gate
The A & B pin should be use as INPUT pin and P pin as an OUTPUT.

---
BAR2308TT as an OR gate
VDD
A(Input)
B(Input)
P = A+B(output)
GND

---
02
Use as AND gate
The A & B pin should be use as INPUT pin and M pin as an OUTPUT.

---
BAR2308TT as an AND gate
VDD
M = A.B(output)
A(Input)
B(Input)
GND

---
03
Use as NOT gate
The C pin should be use as an INPUT pin and N pin as an OUTPUT.

---
BAR2308TT as a NOT gate
VDD
N = C(output)
C(Input)
GND

---
04
Use as NOR gate
The A & B pin should be use as INPUT pin and Q pin as an OUTPUT.

---
BAR2308TT as a NOR gate
VDD
A(Input)
B(Input)
Q = A+B(output)
GND

---
05
Use as NAND gate
The A & B pin should be use as INPUT pin and O pin as an OUTPUT.

---
BAR2308TT as a NAND gate
VDD
A(Input)
O = A.B(output)
B(Input)
GND

---
06
Use as XOR gate
The A & B pin should be use as INPUT pin and X pin as an OUTPUT.

---
BAR2308TT as a XOR gate
VDD
A(Input)
B(Input)
X = A.B+A.B(output)
GND

---
07
Use as XNOR gate
The A & B pin should be use as INPUT pin and W pin as an OUTPUT.

---
BAR2308TT as a XNOR gate
VDD
A(Input)
B(Input)
W = (A.B+A.B)(output)
GND

---
08
Use as Half Adder
The A & B pin should be use as INPUT pin and X(sum) & M(carry) pin as OUTPUT.

---
BAR2308TT as a Half Adder
VDD
M = A.B(CARRY, output)
A(Input)
B(Input)
X = A.B+A.B(SUM, output)
GND

---
SIMPLE DESIGN
This chip layout is Simple design of CMOS. I used here 20 CMOS and connected there as per equation.There is no resistors,inductors,capacitors etc.
COMPUTING POWER
FUNCTIONALITY
Using as a Half adder one can also be able to make a computer(4-bit,8-bit). For that reason, one must be needed multiples BAR2308TT IC chips and needed to add as per equation.
Functionality of this IC chip (BAR2308TT) is very much important. One can use it as similar as any of the Logic gates – OR, AND, NOT, NOR, NAND, XOR, XNOR. He/She can also use it as Half adder.
OPEN SOURCE
It is an Open Source project. Although, I am going to create a License for it, but it will always for public use. Anyone can use it in their projects.

---
Equations
P = A + B
= (A+B)’’
P= Q’
M = A.B
= (A.B)’’
M = O’
N = C’
Q = (A+B)’
O = (A.B)’
X = A.B’ + A’.B
= (A.B’ +A’.B)’’
= ((A.B’)’.(A’.B)’)’
= ((A’+B).(A+B’))’
= (A.A’+A.B+A’.B’+B.B’)’
= (A.B+A’.B’)’
X = (A.B+(A+B)’)’

---
Equations
W = (A.B’ + A’.B)’
= (A.B’)’.(A’.B)’
= (A’+B).(A+B’)
= A.A’+A.B+A’.B’+B.B’
= A.B+A’.B’
= A.B+(A+B)’
= (A.B+(A+B)’)’’
W = X’

---
Simulations

---
Usability
Hope that it’s performance will be incresed.
This will generate many ideas in future.One can use it “All logic gates in one IC chips”.
Yeah, one can definitely share it with anyone.
Due to open source project, It will open to all. Anyone can use it as base chip.
It’s layout should not be changed. I have create a license for it.

---
THANK YOU
AMIT BARMAN
linkdin : @AmitBarman99
twitter : @imamitbarman99
github : @AmitBarman99